Experiment 6

AIM: Write MATLAB codes for finding the Signal Energy or power of signals.

THEORY: Power and Energy content of a signal is often calculated in signal processing for communication applications. For any signal in discrete form, power and energy can be calculated using the following equations:

Energy
The energy of a continuous-time signal x(t) is defined as
E_s = int from -{infinity} to {infinity} {lline x(t) rline}^{2} dt

and the energy of a discrete system is defined as
E_s = sum from n = -{ infinity } to { infinity } {lline x(n) rline}^2

The energy is finite only if the above sum converges to a finite value. This implies that the signal is “squarely-summable”. Such a signal is called finite energy signal.

Power
Power is defined as the amount of energy consumed per unit time. This quantity is useful if the energy of the signal goes to infinity or the signal is “not-squarely summable”.
P_x = lim from {N -> {infinity}} frac{1}{2N + 1} sum from {n = -N} to {n = N} {lline x(n) rline}^2

Classification of Signals:
A signal can be classified based on its power or energy content.
- Energy Signal has finite energy and zero total power.
- Power Signal has finite power and infinite total energy.
- Some signals are neither energy nor power signals.

================================================================

EXERCISE:
Q. Categorize as Energy signal or power signal or otherwise

a) x(t) = left lbrace stack{t,0 le t le 1 # 2 - t, 1 < t le 2 # 0, otherwise} right none

clc;
clearvars;

t = -1:0.00005:3;
x_out = X(t);
x_out = x_out .^ 2;
format long;
area = trapz(t, x_out);
fprintf('Energy is %f\n', area);
fprintf('As Energy is finite, Power is 0\n');

function [t] = X(input)
    t = zeros(1, length(input));
    for i = 1:length(input)
        if(input(i) >= 0 && input(i) <= 1)
        t(i) = input(i);
        elseif(input(i) > 1 && input(i) <= 2)
        t(i) = 2 - input(i);
        else
        t(i) = 0;
        end
    end
end

OUTPUT:

-------------------------------------------------------------------------------------------------------

b) x[n] = left lbrace stack { n, 0 le n < 5 # 10-n, 5 le n le 10 # 0, otherwise} right none

clc;
clearvars;

t = -1:1:11;
x_out = X(t);
x_out = x_out .^ 2;
format long;
area = trapz(t, x_out);
fprintf('Energy is %i\n', area);
fprintf('As Energy is finite, Power is 0\n');

function [n] = X(input)
    n = zeros(1, length(input));
    for i = 1:length(input)
        if(input(i) >= 0 && input(i) < 5)
        n(i) = input(i);
        elseif(input(i) >= 5 && input(i) <= 10)
        n(i) = 10 - input(i);
        else
        n(i) = 0;
        end
    end
end

OUTPUT:

---------------------------------------------------------------------------

c) x(t) = 5cos(%pi t) + sin(5 %pi t), -{infinity} < t < {infinity}

clc;
clearvars;
syms x h;
func = ((5 * cos(pi * x)) + sin(5 * pi * x)) ^ 2;
the_lim = limit((1/(2*h)) * (int(func,x, -h, h)), h, Inf);
fprintf( "\n\rThe power is %i", the_lim)
fprintf( "\nAs it is a power signal, energy is infinite.\n")

OUTPUT:

---------------------------------------------------------------------------

d) x(t) = left lbrace stack{ 5cos(%pi t), -1 le t le 1 # 0, otherwise} right none

clc;
clearvars t xt energy;
t = -1:0.0005:1;
xt = 5 * cos(pi * t);
xt = xt .^ 2;
energy = trapz(t, xt);
fprintf("Energy is %i\n", energy);
fprintf('As Energy is finite, Power is 0\n');

OUTPUT:

---------------------------------------------------------------------------

e) x(t) = left lbrace stack{ cos(%pi t), -0.5 le t le 0.5 # 0, otherwise} right none

clc;
clearvars t xt energy;
t = -0.5:0.000005:0.5;
xt = (cos(pi * t)) .^ 2;
energy = trapz(t, xt);
fprintf("The Energy is %f\n", energy);
fprintf('As Energy is finite, Power is 0\n');

OUTPUT:

---------------------------------------------------------------------------

f) x[n] = left lbrace stack{ sin(%pi n), -4 le n le 4 # 0, otherwise} right none

clc;
clearvars t xt energy;
t = -4:1:4;
xt = abs(sin(pi * t));
xt = xt .^ 2;
energy = sum(xt);
fprintf("This is a zero signal, as energy = %f", energy);

OUTPUT:

---------------------------------------------------------------------------

g) x[n] = left lbrace stack{ cos(%pi n), n ge 0 # 0, otherwise} right none

clc;
clear all;
t = 0:1:400000;
xt = (cos(pi * t)) .^ 2;
ze_sum = sum(xt);
ze_lim = ze_sum / 800001;
fprintf("This is a power signal with power %.5f", ze_lim);

OUTPUT:

---------------------------------------------------------------------------

LEARNING OUTCOME: Learning about energy and power, classification of signals, how to distinguish between energy and power signals and finding the energy and power in MATLAB using various methods including symbolic variables.